## Slide 1: (for inhouse patients)
SUNQUEST
COLLECT

## Slide 2: Log on to Sunquest Collect
Username= Partner’s ID
Password=Sunquest Password
**Note you can not change your password in Collect. This is done in Sunquest.

## Slide 3: Worklist Screen will appear after logging in

## Slide 4: Worklist
Worklist shows patients awaiting collection.
Patients in the configured time frame will appear on the worklist.
The list can be filtered by time range, location, and priority.
The list can be sorted by location, priority, or collection time.

## Slide 5
Claim Button: Claim patients for specimen collection or drop claims that you made previously.
Patient Tabs: All patients shows the number of patient to be displayed and My Patients show patients that are claimed by you.
Order Priority code: This will should the priority the physicians have indicated for each order. Each priority has a color associated with it.
Patient List Icons:
Green indicates patient is claimed by you
Blue icon indicates the patient is claimed by someone else. The
Phlebotomist code will be in Blue.
Test Comment Exists
Another user is in the process of collecting the specimen and the patient is Locked. The user code will appear in above the icon
5. Patient and Order information: Shows Pts name, location and order collection time. If the patient has multiple orders the earliest collection time is shown followed by a number in parentheses indicating the number of orders the patient has.
6. Patient List Filter: Tap to change the sort and filter setting for the patient list. (This will be used when doing morning rounds.)

## Slide 6: Worklist filters

## Slide 7: Draw Prep Screen
If you click once on a patient you will see Draw Prep information to the right.
The blue box around the patient information will indicate which patient you are viewing.

## Slide 8: Getting ready to collect
Make sure you do not have any patients selected prior to scanning a patient bracelet. (If you have a patient selected and it is not the patient you are scanning you will get a warning and will not be able to proceed.) Simply click one more time on the patient and the blue box and draw prep will go away.
Scan your Patients Bracelet

## Slide 9: Patient Collection:
1. Scan the patient’s wristband. The barcode number appears on the screen, and Collect connects with Sunquest Laboratory to retrieve the patient’s information. One of the following occurs:
• The Confirm Patient screen appears.
• A warning message alerts you that the patient ID does not match the patient who is selected on the worklist.
• A scanning error message appears, and you must rescan the patient ID or enter the ID manually. To manually enter the patient ID, proceed to Entering the Patient ID Manually.
2. On the Confirm Patient screen, verify that the patient information displayed matches your patient.
3. Tap Confirm.

## Slide 10: Patient Confirm Screen:
The patient confirmation screen is where you will verbally confirm the patient’s identification. After you complete the verbal confirmation you will select CONFIRM.
NOTE: By selecting confirm you are attesting to the fact that you have followed the patient Identification policy.

## Slide 11: Collect Screen
After Confirming the patient identity and selecting Confirm, you will be brought to the Collect Screen.
Patient information: This area displays the patient’s name, birth date, age, sex, and patient identification number.
Containers required: This area displays the number and type of containers needed for specimen collection. Containers appear in draw order. The area updates automatically after you select or clear a check box next to a container.
Select container check box: Select check boxes for containers you want to collect.
Print : Tap to print labels for the selected containers.
Temporary: Tap to print temporary labels (See guidelines for temporary labels. Note this function will rarely be used at WDH)
1
2
3
4
5

## Slide 12: Collecting and printing labels
After scanning the patients bracelet view the information on the collection screen.
Identify the tubes that are needed for the collection.
Perform venipuncture per policy and best practices.
After the specimen are obtained, select the specimens on the Collections screen by clicking into the container box.
After all the specimen(s) are selected that you have collected, click on PRINT (bottom right hand side of screen)
The Review Screen will appear.

## Slide 13: Review Screen.
The labels will print.
The Review screen will display the specimen you have selected and printed.
The Review screen will ask the following question: Did your labels print?
Either select
  Reprint
OR
  Yes
Affix the labels per policy onto the appropriate containers.
Initial the labels
**NOTE: The date and time of collection is printed on the labels and do not need to be handwritten unless they are cut off or not visible. If the date and time is not visible you must handwrite this information on the labels.**

## Slide 14: Session will end
Once the session times out you will be brought back to the Worklist Screen and you will be ready to go to your next patient.

## Slide 15: Morning Rounds (Additional Information)
Morning rounds
  Filter your collection list by floor, and priority.
  Continue drawing the patients on your designated floors.
  It is important to view all patients on the floor and if you are working with another phlebotomist on the floor you must CLAIM your patients as you go so that the other phlebotomist knows which patient you are going to get.
  After completing your designated refilter your list and look at the whole house to determine who needs assistance.
  Remember when moving to a new floor you should CLAIM the patient you are going to draw.
  After morning rounds are complete (last patient) filter one last time to see if any STATs or additional draws have been added prior to returning to the Main Lab.